## Slide 1
Haptic Sim-Chair Teleoperation
for Autonomous Vehicle Platforms
AVL Summer Cohort 2026
California State Polytechnic University, Pomona
Ryan Simpson · Tyler Carrasco · Yi-Szen Tang · Kevin Xu · Justin Dang
Mentor: Dr. Behnam Bahr
August 7, 2026
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 2
Agenda
1. Project overview
2. Technical architecture
3. Methodology (how we built it)
4. Challenges and solutions
5. Results and metrics
6. Demo summary
7. Future work
8. Handoff / Q&A
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 3
Overview: The Problem
Remote drivers lose the cues that make driving intuitive:
- Peripheral vision and depth
- Body motion / acceleration feel
- Confident, precise control
Flat single-camera teleop is not enough for hazardous sites or AV safety intervention.
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 4
Overview: Our Solution
Marvin go-kart ↔ D-BOX sim chair over Tailscale VPN
Channel | What it restores
Vision | 3× ZED X → 3 panoramic monitors
Control | Thrustmaster wheel/pedals → differential drive
Haptics | IMU → D-BOX chair (bridge ready; E2E verify next)
Goal: human-level sight + physical feedback at internet scale.
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 5
Overview: Current Status
Capability | Status
Wheel/pedal remote drive | Working
3-camera live JPEG video | Working (UDP primary)
D-BOX SDK on Windows | Working
Vehicle IMU → chair E2E | Script ready: verify live
Motor sustained quality | Open issue
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 6
Technical Architecture
OPERATOR (Windows) TAILSCALE VEHICLE (Jetson)
Wheel/Pedals --> UDP :5006 --------------------> controller -> Teensy -> Motors
3 Monitors <-- UDP :9001-3 <------------------ ZED X x3 -> camera_sender_udp
D-BOX <-- UDP :5007 <-------------------- IMU bridge (Xsens)
Status <-- UDP :5008 <-------------------- controller status
Primary video path: chunked JPEG over UDP (~1280×720 @ 30). TCP JPEG is legacy fallback.
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 7
Technical Architecture: Stack
Operator: Windows · SDL2 · OpenCV · D-BOX LiveMotion · Tailscale 100.91.25.107
Vehicle: Jetson Orin · Ubuntu 22.04 · ROS 2 Humble · CycloneDDS · domain 42 · 100.93.121.3
Actuation: Teensy 4.1 @ 115200 → REV Spark MAX (differential drive)
Key apps: simchair_sender_dbox.exe · orin_vehicle_controller.py · orin_camera_sender_udp.py · imu_bridge.py · windows_camera_receiver_udp.py
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 8
Methodology
1. Keep teleop outside shared IGVC tree (read-only)
2. Prefer reliable demo path (UDP JPEG; TCP fallback) over unfinished codecs
3. Forward ZED compressed topics (no re-encode)
4. Stagger ZED launches; unset DISPLAY; TF/URDF on
5. OpenCV display main thread only on Windows
6. Measure: Tailscale RTT + glass-to-glass stopwatch (10 samples)
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 9
Challenges & Solutions
Challenge | Solution
ZED EGL / Argus crash | Real unset DISPLAY (not empty string)
No frames / TF hang | publish_tf:=true publish_urdf:=true
Dual ZED stacks fight | One stack only; kill watchdogs
Multi-cam crash | 25 s stagger between cameras
OpenCV blank windows | Main-thread imshow + queues
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 10
Challenges & Solutions (cont.)
Challenge | Solution
GStreamer RTSP unreliable | Adopt JPEG (TCP then UDP chunked) as primary
Control inverted | Fix throttle-brake and steering signs
Conda breaks ROS Python | Always /usr/bin/python3
Tailscale MTU 1280 | UDP chunks ≤1200 bytes
Still open: motor degradation, right-tilt, IMU→chair E2E, DERP vs direct.
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 11
Results: Verified Capabilities
- Remote drive from sim chair over Tailscale
- Three live camera streams on Surround monitors
- D-BOX SDK integrated (local input cueing)
- Reproducible full-stack launch (orin_launch_all.sh)
Baseline date: 2026-07-27 · TCP video 2026-08-04 · UDP JPEG primary 2026-08-07
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 12
Results: Baseline Metrics
Metric | Value | Target
Tailscale RTT | 88-112 ms (DERP) | Direct peer path
Video | 1280×720 @ 30 JPEG/UDP (target) | H.265 / higher res
Glass-to-glass | TBD | <150 ms median
Control rate | ~20 Hz | 50 Hz + seq/watchdogs
Bandwidth (3 cams) | TBD | <25 Mbps
*Do not invent TBD numbers: measure before claiming.*
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 13
Demo Summary
What you see: operator in D-BOX chair → panoramic video → kart responds to wheel
Verified path tonight:
1. Jetson: orin_launch_all.sh
2. Windows: start_all.bat or windows_camera_receiver_udp.py + simchair_sender_dbox.exe
Do not claim unless checked live: H.265 primary, <150 ms G2G, full IMU→chair washout, perfect sustained motors.
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 14
Future Work (Priority Order)
1. Motors: degradation and right-tilt
2. IMU → D-BOX end-to-end + washout tuning
3. H.265 / higher res video
4. Latency on direct Tailscale (<150 ms)
5. Control seq + multi-layer watchdogs
6. systemd + persistent firewall + soak ≥30 min
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 15
Codebase & Handoff
cursor-test/windows/ <- launch Windows apps
cursor-test/jetson/ <- push to ~/Documents/SimChair_Teleop/
cursor-test/docs/ <- architecture, launch, known issues
Never modify /home/dinosaur/IGVC/
See: docs/deliverables/HANDOFF_PACKAGE.md · docs/LAUNCH_PROCEDURE.md · docs/KNOWN_ISSUES_AND_HISTORY.md
Marvin Sim Chair · AVL Summer Cohort 2026

## Slide 16
Thank You
Questions?
Team: Ryan Simpson (lead) · Tyler Carrasco · Yi-Szen Tang · Kevin Xu · Justin Dang
Mentor: Dr. Behnam Bahr · AVL, Cal Poly Pomona
Deliverables: Technical report · This deck · Demo video · Handoff package
Submit To: mghasemi@cpp.edu · CC: rmsimpson@cpp.edu, kbraga@cpp.edu
Marvin Sim Chair · AVL Summer Cohort 2026